## Slide 1: FA25ProgressReport_Lucas
2025/11/24

## Slide 2: Interlocking Topology
Geometric Classification
Segments are classified into four mechanical categories based on their orientation angle relative to the horizontal axis:
Quantitative Descriptors
Calculates key metrics to quantify mechanical strength potential:
Category | Classification | Angle Range (θ) | Function / Surface Type
1 | Horizontal |  | Primary Interlock Surface
2 | Closing |  | Adhesion Interface (Closing)
3 | Opening Upper |  | Adhesion Interface (Opening)
4 | Opening Lower |  | Adhesion Interface (Opening)
Category | Classification | Angle Range (θ) | Function / Surface Type
1 | Horizontal |  | Primary Interlock Surface
2 | Closing |  | Adhesion Interface (Closing)
3 | Opening Upper |  | Adhesion Interface (Opening)
4 | Opening Lower |  | Adhesion Interface (Opening)
SAEF | Surface Area Enhancement Factor | The ratio of total actual interface length to the projected seam length ().
MID | Mechanical Interlocking Depth | The maximum amplitude of the interface in the interlocking direction (X-axis span).
VIR | Volumetric Interlock Ratio | Normalized ratio representing the effective geometric overlap area relative to the bounding box defined by MID and projected length.
SAEF | Surface Area Enhancement Factor | 
MID | Mechanical Interlocking Depth | The maximum amplitude of the interface in the interlocking direction (X-axis span).
VIR | Volumetric Interlock Ratio | Normalized ratio representing the effective geometric overlap area relative to the bounding box defined by MID and projected length.
Coded an automated process that used a traversal method from top to bottom to classify and label segments, calculates the sum of the segment lengths in each image, and uses this to compute three Geometric Descriptors.

## Slide 3: Interlocking Topology
Found 15 valid segments.
--- Segment Statistics (mm) ---
Total CAT_HORIZONTAL Length: 0.1093
Total CAT_CLOSING Length: 2.2933
Total CAT_OPENING_UPPER Length: 1.2516
Total CAT_OPENING_LOWER Length: 0.0000
--- Geometric Descriptors ---
SAEF: 1.5709
MID: 0.6307 mm
VIR: 0.2299
Categorized and Labeled Segments
Statistics Output

## Slide 4: Learning FEA Workflow — Mixed mesh model Simulation and Optimisation
Mesh generation and combination
Geometry Input
(Piecewise Linear Complex)
Triangular Surface Mesh
Volumetric Tetrahedral Mesh
{

## Slide 5
Tetrahedral Mesh Workflow

## Slide 6: Pyvista – Tetgen – gmsh – FEniCS Toolchain Result Visualisation in Paraview
Von Mises stress plot
Displacement (Z) plot